Brief
This document assumes that you have read through the Conkit User Documentation or are at least vaguely familiar with the application of the conkit.h header.

List of Definitions within conkit.h
Items wholly relevant to the user will have their name in blue:
Name	Classification	Datatype	Platform	Description
struct ck_console_size	struct (datatype)	struct { / size_t width, / height; / _Bool has_changed; / };	Both	Return type of ck_current_console_size(): width = current console width (columns), height = current console height (lines), has_changed = does the width or height differ from last time ck_current_console_size() was invoked?
CK_SCREEN_BUFFER_SIZE	global	size_t	Both	Size of CK_SCREEN_BUFFER, in characters
CK_SCREEN_BUFFER_END	global	size_t	Both	Index of last character printed to CK_SCREEN_BUFFER.
CK_SCREEN_BUFFER	global	char *	Both	Buffer to which all printing intended for output should be done, so that it can all be outputted in one go once the drawing process is complete.
CK_SEQUENCE_BUFFER	global	char *	Both	Buffer to which strings containing ANSI escape-sequences are written in the non-literal-argument implementations of the sequence-generation functions. Note that because this buffer is shared between all of these functions, successive writes by each of them will overwrite the contents of the buffer. This means that calling these functions for a return value as an argument to a surrounding function-call will result in only the last call’s generated sequence being used as the string for each of the others. literal-argument implementations do not suffer from this issue as they do not use a buffer. To avoid this issue, maybe something like strdup() on the return value of the function would be advisable, should you wish to use them in-sequence.
CK_ALLOC_SIZE	global constant	Macro: #define CK_ALLOC_SIZE	Both	Indicates an amount of chars that buffer sizes will start at and be reallocated by should they need it. Consequently, the larger this size is, the faster your program will be with initial writes to buffers as less reallocation will be required, but the more memory will be used.
CK_STD_OUTPUT_HANDLE	global	HANDLE	Windows	Handle for Standard Output that is used to enable ANSI escape-sequences and acquire the size of the console.
CK_CONSOLE_MODE	global	DWORD	Windows	Console mode DWORD for enabling ANSI escape sequences and eventually resetting the modes back to the way they were.
sleep()	function	Macro: #define sleep(ms)	Both	Function to sleep a number of milliseconds, wrapped as sleep(), backending to either usleep() or Sleep() depending on the platform.
ck_init()	function	Function: void ck_init(void)	Both	Initialises Conkit, allocating memory for buffers and performing implementation-specific tasks and pre-computations.
ck_end()	function	Function: void ck_end(void)	Both	Frees memory and performs necessary reversions after Conkit is no longer needed.
ck_current_console_size()	function	Function: struct ck_console_size ck_current_console_size(void)	Both	Returns the current width and height of the console, measured in lines and columns of characters, and additionally whether these values have changed since the last call to this function was performed.
CK_CONSOLE_SETTS	global	struct termios	Unix-like	Non-buffered, non-echoed configuration-attribute for usage by getch() and kbhit() implementations.
CK_CONSOLE_ORIG_SETTS	global`	struct termios	Unix-like	Original configuration-attribute for the console used to restore the existing configuration once usage of the terminal in the / CK_CONSOLE_SETTS configuration is complete, within the runtime of the getch() and kbhit() functions.
ck_rgb()	function	Function: char *ck_rgb(unsigned char where, unsigned char r, / unsigned char g, unsigned char b)	Both	Non-literal-argument sequence-generation function for setting terminal to output in a certain (r, g, b) colour.
ck_bg_rgb()	function	Macro: #define ck_bg_rgb(r, g, b)	Both	Non-literal-argument sequence-generation function for setting the terminal background colour to a certain (r, g, b) value.
ck_fg_rgb()	function	Macro: #define ck_bg_rgb(r, g, b)	Both	Non-literal-argument sequence-generation function for setting the terminal foreground colour to a certain (r, g, b) value.
ck_cursor_goto()	function	Function: char *ck_cursor_goto(size_t x, size_t y)	Both	Non-literal-argument sequence-generation function for moving the cursor in the console such that it may print at a specified set of co-ordinates (x, y). x is 0-… and goes from left to right, y is 0-… and goes from top to bottom.
ck_cursor_move()	function	Function: char *ck_cursor_move(char where, size_t amount)	Both	Non-literal-argument sequence-generation function for moving the cursor on the console in a specific direction relative to its current position, by a specified amount.
ck_cursor_up()	function	Macro: #define ck_cursor_up(amount)	Both	Non-literal-argument sequence-generation function for moving the cursor on the console upward by a specified amount.
ck_cursor_down()	function	Macro: #define ck_cursor_down(amount)	Both	Non-literal-argument sequence-generation function for moving the cursor on the console downward by a specified amount.
ck_cursor_left()	function	Macro: #define ck_cursor_left(amount)	Both	Non-literal-argument sequence-generation function for moving the cursor on the console leftward by a specified amount.
ck_cursor_right()	function	Macro: #define ck_cursor_right(amount)	Both	Non-literal-argument sequence-generation function for moving the cursor on the console rightward by a specified amount.
ck_bg_rgb_l()	function	Macro: #define ck_bg_rgb_l(r, g, b)	Both	Equivalent of ck_bg_rgb(), but preferable to that if the arguments will be literals, due to less overhead.
ck_fg_rgb_l()	function	Macro: #define ck_fg_rgb_l(r, g, b)	Both	Equivalent of ck_fg_rgb(), but preferable to that if the arguments will be literals, due to less overhead.
ck_cursor_goto_l()	function	Macro: #define ck_cursor_goto_l(r, g, b)	Both	Equivalent of ck_cursor_goto(), but preferable to that if the arguments will be literals, due to less overhead.
ck_cursor_up_l()	function	Macro: #define ck_cursor_up_l(amount)	Both	Equivalent of ck_cursor_up(), but preferable to that if the arguments will be literals, due to less overhead.
ck_cursor_down_l()	function	Macro: #define ck_cursor_down_l(amount)	Both	Equivalent of ck_cursor_down(), but preferable to that if the arguments will be literals, due to less overhead.
ck_cursor_left_l()	function	Macro: #define ck_cursor_left_l(amount)	Both	Equivalent of ck_cursor_left(), but preferable to that if the arguments will be literals, due to less overhead.
ck_cursor_right_l()	function	Macro: #define ck_cursor_right_l(amount)	Both	Equivalent of ck_cursor_right(), but preferable to that if the arguments will be literals, due to less overhead.
ck_print()	function	Function: void ck_print(char *buffer)	Both	Allows the writing of a string to the CK_SCREEN_BUFFER, so that it may be sent to stdout when ck_flip() is eventually called.
ck_flip()	function	Function: void ck_flip(void)	Both	Print the contents of the CK_SCREEN_BUFFER, starting at (0, 0) on the console, and subsequently clear it.
getch()	function	Function: char getch(void)	Both	Get 1 character of input without printing the character to the console when it is typed-out, or waiting for a newline to return.
kbhit()	function	Function: _Bool kbhit(void)	Both	Returns whether there is any input on stdin.

Pseudocode

Initial Definitions

>> Type definition of ck_console_size

structure ck_console_size
width is integer
height is integer
has_changed is boolean
end structure

>> Definition (and initialisation of some) globals

if on_windows then
CK_STD_OUTPUT_HANDLE is HANDLE
CK_CONSOLE_MODE is DWORD
else if on_unix then
CK_CONSOLE_SETTS is structure termios
CK_CONSOLE_ORIG_SETTS is structure termios
else
raise_error_during_compilation()
end if

CK_ALLOC_SIZE is integer

CK_SCREEN_BUFFER_SIZE is integer
CK_SCREEN_BUFFER_END is integer
CK_SCREEN_BUFFER is string

CK_SEQUENCE_BUFFER is string

CK_ALLOC_SIZE = 100

Function Definitions with Implementation-Specific Constructs

>> Definition of ck_init()

function ck_init()
if on_windows then
CK_STD_OUTPUT_HANDLE = standard_output_handle_of_current_environment()
CK_CONSOLE_MODE = mode_of(CK_STD_OUTPUT_HANDLE)
set_mode_for_current_environment(
enable_ansi_escape_codes(CK_CONSOLE_MODE))
else if on_unix then
CK_CONSOLE_ORIG_SETTS = current_console_settings()
CK_CONSOLE_SETTS =
buffering_and_input_echoing_disabled(CK_CONSOLE_ORIG_SETTS)
end if

CK_SCREEN_BUFFER = string_of_size(CK_ALLOC_SIZE)
CK_SCREEN_BUFFER_END = 0
CK_SCREEN_BUFFER_SIZE = CK_ALLOC_SIZE

CK_SEQUENCE_BUFFER = string_of_size(maximum_escape_sequence_length())
end function

>> Definition of ck_end()

function ck_end()
if on_windows then
set_mode_for_current_environment(CK_CONSOLE_MODE)
end if

free_memory(CK_SCREEN_BUFFER)
free_memory(CK_SEQUENCE_BUFFER)
end function

>> Definition of getch() and kbhit()

if on_windows then
put_contents_of_file_here(“conio.h”)
else if on_unix then
function getch()
ret is character

set_current_console_settings(CK_CONSOLE_SETTS)

input ret

set_current_console_settings(CK_CONSOLE_ORIG_SETTS)

return ret
end function

function kbhit()
pollResults is structure poll

set_current_console_settings(CK_CONSOLE_SETTS)

pollResults = poll(standard_input_stream)

set_current_console_settings(CK_CONSOLE_ORIG_SETTS)

return bit_mask(pollResults, input_was_found)
end function
end if

>> Definition of ck_current_console_size()

function ck_current_console_size()
knownSize is variable_with_value_preserved_between_function_calls of_type structure ck_console_size
newWidth is integer
newHeight is integer

run_section_when_it_is_the_first_call_to_the_function
knownSize.has_changed = false
knownSize.width = 0
knownSize.height = 0
end run_section_when_it_is_the_first_call_to_the_function

if on_windows then
newWidth = screen_info(CK_STD_OUTPUT_HANDLE).right –	screen_info(CK_STD_OUTPUT_HANDLE).left +
        1
newHeight = screen_info(CK_STD_OUTPUT_HANDLE).bottom -
        screen_info(CK_STD_OUTPUT_HANDLE).top +
        1
else if on_unix then
newWidth = screen_info().width
newHeight = screen_info().height
end if

knownSize.has_changed = newWidth != knownSize.width or
        newHeight != knownSize.height

if knownSize.has_changed then
knownSize.width = newWidth
knownSize.height = newHeight
end if

return knownSize
end function

>> Definition of sleep()

if on_windows then
function sleep(milliseconds is integer)
Sleep(milliseconds)
end function
else if on_unix then
function sleep(milliseconds is integer)
usleep(milliseconds * 1000)
end function
end if

Functions that are Defined the Same on Both Platforms

Non-Literal-Argument Sequence-Generation Functions

>> Definitions of rgb functions

function ck_rgb(bg_or_fg is integer,
   r is integer,
   g is integer,
   b is integer)

CK_SEQUENCE_BUFFER = “\033[{bg_or_fg};2;{r};{g};{b}m”

return CK_SEQUENCE_BUFFER
end function

function ck_bg_rgb(r is integer,
        g is integer,
        b is integer)
return ck_rgb(48, r, g, b)
end function

function ck_fg_rgb(r is integer,
        g is integer,
        b is integer)
return ck_rgb(38, r, g, b)
end function

>> Definitions of cursor-movement functions

function ck_cursor_goto(x is integer, y is integer)
CK_SEQUENCE_BUFFER = “\033[{y};{x}H”

return CK_SEQUENCE_BUFFER
end function

function ck_cursor_move(direction is character, amount is integer)
CK_SEQUENCE_BUFFER = “\033[{amount}{direction}”

return CK_SEQUENCE_BUFFER
end function

function ck_cursor_up(amount is integer)
return ck_cursor_move(‘A’, amount)
end function

function ck_cursor_down(amount is integer)
return ck_cursor_move(‘B’, amount)
end function

function ck_cursor_left(amount is integer)
return ck_cursor_move(‘D’, amount)
end function

function ck_cursor_right(amount is integer)
return ck_cursor_move(‘C’, amount)
end function

Literal-Argument Sequence-Generation Functions

>> Definitions of rgb functions

function ck_bg_rgb_l(r is literal, g is literal, b is literal)
return compile_time_string(“\033[48;2;{r};{g};{b}m”)
end function

function ck_fg_rgb_l(r is literal, g is literal, b is literal)
return compile_time_string(“\033[38;2;{r};{g};{b}m”)
end function

>> Definitions of cursor-movement functions

function ck_cursor_goto_l(x is literal, y is literal)
return compile_time_string(“\033[{y};{x}H”)
end function

function ck_cursor_up_l(amount is literal)
return compile_time_string(“\033[{amount}A”)
end function

function ck_cursor_down_l(amount is literal)
return compile_time_string(“\033[{amount}B”)
end function

function ck_cursor_left_l(amount is literal)
return compile_time_string(“\033[{amount}D”)
end function

function ck_cursor_right_l(amount is literal)
return compile_time_string(“\033[{amount}C”)
end function

Functions Concerning the Screen Buffer

>> Definition of ck_print()

function ck_print(buffer is string)
while CK_SCREEN_BUFFER_END + buffer.length + 1 > CK_SCREEN_BUFFER_SIZE
CK_SCREEN_BUFFER_SIZE = CK_SCREEN_BUFFER_SIZE + CK_ALLOC_SIZE
end while

CK_SCREEN_BUFFER_END = CK_SCREEN_BUFFER_END + buffer.length + 1

CK_SCREEN_BUFFER = string_of_changed_size(CK_SCREEN_BUFFER_SIZE)

CK_SCREEN_BUFFER = CK_SCREEN_BUFFER + buffer
end function

>> Definition of ck_flip()

function ck_flip()
output “\033[H”, CK_SCREEN_BUFFER

clear_string(CK_SCREEN_BUFFER)
CK_SCREEN_BUFFER_END = 0
end function